## Slide 1
Critical Issue Status — 2026-03-26
Source: Jira filter "SW 12.1.2 Targeted P0/P1 Bugs" (33573) | 33 bugs: 23 P0, 10 P1 | 20 active, 9 Verify, 4 Closed
Open Critical | New This Week | Waiting for Verify in DST | Actively Root-Causing
20 | 5 | 9 | 12
Area | Issues | Description | Customer | Status | Next Steps
BTS / Lustre | STL-76950 STL-76880 STL-76940 | GPU DMA-buf deregistration race — mi300x kernel panics in rdmavt + Lustre RDMA timeouts with BTS. All hit same BTS memory lifecycle path. | — | In Review / In Progress | 76950 fix in review (Child); depends on 1 sub-fix in Verify + 2 still Open. If all land → cascade-fixes cluster.
OPX — TID cache | STL-76365 STL-73247 | OPX TID cache diverges from kernel TID table under high expected-receive rate. HPL + sph_exa hangs. Chronic — 73247 open since 12.1.0.x. | — | In Progress | Architecturally complex fix spanning OPX user-space + hfi1 kernel. Cernohous + Erwin.
OPX — GPU AI | STL-77071 | MPT-30B hang with aws-ofi dmabuf. May overlap BTS DMA-buf cluster. New this week. | RWTH | Open | Espinoza assessing. Possible user config issue — engaging customer.
OPX — Perf | STL-76240 | IMB Biband/Sendrecv perf drop starting at OPXS 12.1.0.0-62. Data path regression on AMD. | AMD | In Progress | Simonson bisecting OPX builds to isolate regression commit.
OPX / Lustre | STL-77023 | Endeavour Lustre problems with use_bulksvc=N — fails even without BTS. New this week. | Intel | Open | Child assessing. Waiting on dmesg from Intel.
Fabric / MYR FW | STL-76338 STL-76494 STL-76725 STL-75962 | MYR switch buffer/credit mgmt — tportPktDropPending, RbufCtrlSbe, TxHoqDiscards, credit exhaustion. All related switch-side failures. | TACC | In Progress | Wright on ISL drops. Rothermel on RbufCtrlSbe. King on HoQ discards. No fixes landed yet.
Fabric / MYR FW | STL-77092 | DWC switch VR fault on liquid-cooled switch. HW issue, separate from buffer/credit. New this week. | Lenovo | In Review | Nagarajan fix in review.
Host Driver — IPoIB | STL-76836 STL-74848 | ipoib timeout + SDMA Tx queue stalls. 74848 has sw_fixed. 76836 may be fabric-caused (links to 76494 + 76873). | LLNL (Lynx) | Open / In Progress | Test 74848 SDMA fix first. If unresolved, root cause is likely fabric-side.
Host Driver — PCIe | STL-75661 STL-76323 STL-76997 | Cards failing init after power events + runtime PCIe fatal errors under SPEC. All PCIe / 8051 FW path. | Lenovo, IOCB, NEC/RWTH | Open / In Progress | Davis on IOCB. Luick on SPEC crash. 75661 needs pickup (Zhang, Open).
Link / 8051 FW | STL-76873 | Link fails LNI during EstablishComm.TxRxHunt — 8051 FW SerDes link training failure. ~8 links affected. | LLNL (Lynx) | In Progress | Johanson leading via Link Working Group.
Chassis | STL-77046 | BMC FruDevice introspect fail — switch buggy state after bounce+reboot testing. Not data-path. New this week. | — | Ready | Queued for Nagarajan.

## Slide 2
BTS / Lustre — Detail
3 active + 6 in Verify — BTS memory deregistration race is the core root cause
Active (3 bugs)
Issue | Pri | Summary | Assignee | Status | Root Cause / Blockers | Next Steps
STL-76950 | P0 | mi300x crash on ctl-c BTS/dmabuf — bulksvc_user_info_destroy | Child | In Review | GPU DMA-buf deregistration race. Blocked by: STL-76982 (DMS unregister, Verify) STL-76983 (force-cancel trackers, Open) STL-76984 (rvt/bulksvc race, Open) | Retest with next DST once all 3 blockers land.
STL-76880 | P0 | mi300x GPU kernel panic rvt_send_complete | Simonson | In Progress | Same rdmavt DMA-buf path as 76950. | Likely fixed by 76950 patches. Retest together.
STL-76940 | P0 | LNetError RDMA timeout with BTS — Lustre client eviction | Simonson | In Progress | Lustre ko2iblnd hits BTS verbs path. Caused by STL-76941 (Verify). Blocked by STL-76999 (Verify). | Zhu: "Wait for 12.1.2 DST — fixed a few bugs."
Verify Queue (6 BTS fixes awaiting validation)
Issue | Summary | What It Fixes
STL-76982 | Rearchitect DMS unregister to be always-async | Blocks 76950 (DMA-buf crash)
STL-76999 | Fix bulksvc_dbg_open unbounded spin-wait deadlock | Blocks 76940 (Lustre RDMA timeout)
STL-76941 | hfi1_dms_handle_data crash | Causes 76940 (Lustre RDMA timeout)
STL-76863 | BAD WRITE CHECKSUM — BTS MR registration error | BTS Lustre data integrity
STL-76847 | calculate_mr_page_offset Invalid | BTS Lustre data integrity
STL-76942 | bufcount error — BTS buffer management | BTS Lustre data integrity
STL-76732 | hfi1_dms_impl_dlist_remove crash — DMS list corruption | BTS internal locking

## Slide 3
OPX — Detail
5 active + 2 in Verify — TID cache is chronic; perf regression + 2 new bugs this week
Active (5 bugs)
Issue | Pri | Summary | Assignee | Status | Customer | Root Cause | Next Steps
STL-76365 | P0 | HPL hang in hfi1_user_exp_rcv_setup | Cernohous | In Prog | — | OPX TID cache diverges from kernel. Links to 76561, 76972, 76685, 76554. | Fix spans OPX user-space + hfi1 kernel.
STL-73247 | P0 | sph_exa hang with OPX Open MPI | Erwin | In Prog | — | Same TID cache root cause. Open since 12.1.0.x. | Same fix as 76365.
STL-77071 | P0 | MPT-30B hang aws-ofi dmabuf | Espinoza | Open | RWTH | Possibly OPX+DMA-buf. May be user config. | Engaging RWTH directly.
STL-76240 | P1 | IMB Biband/Sendrecv perf drop | Simonson | In Prog | AMD | OPX data path regression in 12.1.0.0-62+. Blocks 76449, 77018, 76861. | Bisecting OPX builds.
STL-77023 | P1 | Endeavour Lustre use_bulksvc=N | Child | Open | Intel | Lustre fails without BTS. Separate root cause. | Waiting on dmesg from Intel.
Verify Queue (2 OPX fixes)
Issue | Summary | What It Fixes
STL-76561 | HPL OPX_TID_CACHE assert with use_bulksvc:N | Related to TID cache cluster (76365, 73247)
STL-76644 | NEC IMB-RMA SDMA abort — OPX rendezvous path | OPX data path correctness

## Slide 4
Fabric / MYR FW — Detail
5 active — Buffer/credit cluster is riskiest area (4 bugs, zero fixes landed)
Active (5 bugs)
Issue | Pri | Summary | Assignee | Status | Customer | Root Cause | Next Steps
STL-76338 | P0 | tportPktDropPending hang on ISL bounce | Wright | In Prog | TACC | MYR Tport state machine. Links to 76651, 76652, ISS-8041. | Reproduced internally. Wright analyzing.
STL-76494 | P0 | Hung nodes — RbufCtrlSbe ECC errors | Rothermel | In Prog | TACC | SRAM bit errors corrupt buffer mgmt. sw_fixed label. Links to 76836, 77090. | SW workaround exists. Watch SBE rate for HW degradation.
STL-76725 | P1 | Excessive TxHoqDiscards | King | In Prog | TACC | Head-of-queue blocking, same credit subsystem. Links to 75822. | Reproduced with synthetic ISL saturation.
STL-75962 | P1 | Job hang — MYR Tport credit exhaustion | Rothermel | In Prog | — | Transport credit accounting. Links to 75847. | Credit accounting analysis in progress.
STL-77092 | P0 | DWC switch VR fault (liquid-cooled) | Nagarajan | In Review | Lenovo | Voltage regulator HW fault. Separate from buffer/credit. | Fix in review.

## Slide 5
Host Driver — Detail
5 active + 2 in Verify — 76836 (LLNL ipoib) may be fabric-caused, not host driver
Active (5 bugs)
Issue | Pri | Summary | Assignee | Status | Customer | Root Cause | Next Steps
STL-76836 | P0 | ipoib timeout at LLNL Lynx | Novak | Open | LLNL | IPoIB/SDMA path. BUT: links to 76494 (RbufCtrlSbe) + 76873 (link training). May be fabric-caused. | Test 74848 SDMA fix first. If no fix, reclassify as fabric.
STL-74848 | P1 | SDMA Tx queue timeout — no descriptors | Hwang | In Prog | — | SDMA descriptor exhaustion. sw_fixed label. | Fix ready. Retest in next DST.
STL-76997 | P0 | Job crashes during SPEC run | Luick | Open | NEC/RWTH | Relates to 75193 (PCIe fatal error). Investigating uncorrectable error correlation. | Koch providing lspci. Luick proceeding with investigation.
STL-75661 | P1 | Link not Active after power-cycle | Zhang | Open | Lenovo | 8051 FW / JKR FW PCIe init. Card fails to enumerate. | NEEDS PICKUP — Open, no recent activity.
STL-76323 | P1 | PCIe enumeration / HFI init failures | Davis | In Prog | IOCB | Same PCIe init path as 75661. 5/204 jobs failing. | Davis actively investigating. Repro rate reduced.
Verify Queue (2 Host Driver fixes)
Issue | Summary | What It Fixes
STL-77078 | Nightly CI IB Verbs Atomic BW failure | CI regression
STL-76108 | SRIOV VMs cannot query SA — sw_fixed | SRIOV connectivity

## Slide 6
Link / 8051 FW + Chassis — Detail
2 active — Link training at LLNL + BMC management issue
Active (2 bugs)
Issue | Pri | Summary | Assignee | Status | Customer | Root Cause | Next Steps
STL-76873 | P0 | Link fails LNI during EstablishComm.TxRxHunt | Johanson | In Prog | LLNL | 8051 FW SerDes link training. ~8 links not coming up. Links to 76836 (ipoib). | Johanson leading via Link Working Group.
STL-77046 | P1 | BMC FruDevice introspect fail — buggy state | Nagarajan | Ready | — | Chassis mgmt. After ~17h link bounce + reboot test. Not data-path. | Queued for Nagarajan.

## Slide 7
Root Cause Cluster Summary
20 active bugs → 7 root causes + 5 standalone
# | Root Cause | Active | Verify | Closed | Fix One, Fix All?
1 | BTS DMA-buf deregistration race | 3 | 6 | 1 | Yes — 76950 fix in review → cascade-fixes. But 2 of 3 blockers still Open.
2 | OPX TID cache kernel divergence | 2 | 1 | — | Yes — same arch fix. Complex (user + kernel).
3 | MYR buffer/credit switch FW | 4 | — | — | Partially — related but may need separate fixes. Zero resolved.
4 | IPoIB / SDMA transmit | 2 | — | — | Maybe — 74848 sw_fixed may resolve 76836.
5 | PCIe / card init | 3 | — | — | Partially — 75661 + 76323 same path, 76997 is runtime.
6 | OPX GPU AI | 1 | — | 2 | TBD — 77071 may be user config.
7 | OPX perf regression | 1 | 1 | 1 | Separate — bisecting to isolate commit.
8 | Link training 8051 FW | 1 | — | — | Standalone. Link WG owns.
— | Standalone (Lustre non-BTS, VR, BMC, CI, SRIOV) | 4 | 2 | — | Each separate.
1. BTS is #1 area — 3 active + 6 in Verify. 76950 fix depends on 2 patches still Open (76983, 76984). Next DST is the gate.
2. MYR buffer/credit is riskiest — 4 bugs, all In Progress, zero fixes landed. TACC is primary customer.
3. 76836 (LLNL ipoib) may be fabric-caused — test SDMA fix first; if no resolution, reclassify.
4. OPX TID hangs still chronic — 73247 open since 12.1.0.x. Architecturally complex fix.
5. 75661 (Lenovo power-cycle) needs pickup — assigned to Zhang, Open, no recent activity.