## Slide 1
Critical Issue Status (P0 Only) — 2026-03-26
Source: Jira filter "SW 12.1.2 Targeted P0 Bugs" (33606) | 23 P0 bugs: 12 active, 6 Verify, 5 Closed
Open Critical | New This Week | Waiting for Verify in DST | Actively Root-Causing
12 | 3 | 6 | 7
Area | Issues | Description | Customer | Status | Next Steps
BTS / Lustre | STL-76950 STL-76880 STL-76940 | GPU DMA-buf deregistration race — mi300x kernel panics in rdmavt + Lustre RDMA timeouts. All hit same BTS memory lifecycle path. | — | In Review / In Progress | 76950 fix in review (Child); blocked by 76982 (Verify) + 76983, 76984 (Open). If all land → cascade-fixes cluster.
OPX — TID cache | STL-76365 STL-73247 | OPX TID cache diverges from kernel TID table under high expected-receive rate. HPL + sph_exa hangs. Chronic — 73247 open since 12.1.0.x. | — | In Progress | Architecturally complex fix spanning OPX user-space + hfi1 kernel. Cernohous + Erwin.
OPX — GPU AI | STL-77071 | MPT-30B hang with aws-ofi dmabuf. May overlap BTS DMA-buf cluster. New this week. | RWTH | Open | Espinoza assessing. Possible user config issue — engaging customer.
Fabric / MYR FW | STL-76338 STL-76494 | MYR switch buffer/credit mgmt — tportPktDropPending on ISLs, RbufCtrlSbe hung nodes. 76494 has sw_fixed workaround. | TACC | In Progress | Wright on ISL drops. Rothermel on RbufCtrlSbe. No fixes landed yet.
Fabric / MYR FW | STL-77092 | DWC switch VR fault on liquid-cooled switch. HW issue, separate from buffer/credit. New this week. | Lenovo | In Review | Nagarajan fix in review.
Host Driver — IPoIB | STL-76836 | ipoib timeout at LLNL Lynx. May be fabric-caused — links to 76494 (RbufCtrlSbe) + 76873 (link training). | LLNL (Lynx) | Open | Correlate with fabric cluster. If fabric-side, reclassify.
Host Driver — PCIe | STL-76997 | Jobs crashed during SPEC run at NEC/RWTH. PCIe uncorrectable error correlation. Relates to STL-75193. | NEC/RWTH | Open | Luick investigating. Koch providing lspci output.
Link / 8051 FW | STL-76873 | Link fails LNI during EstablishComm.TxRxHunt — 8051 FW SerDes link training. ~8 links affected. | LLNL (Lynx) | In Progress | Johanson leading via Link Working Group.

## Slide 2
BTS / Lustre — Detail
3 active + 5 in Verify — BTS memory deregistration race is the core root cause
Active (3 bugs)
Issue | Pri | Summary | Assignee | Status | Root Cause / Blockers | Next Steps
STL-76950 | P0 | mi300x crash on ctl-c BTS/dmabuf — bulksvc_user_info_destroy | Child | In Review | GPU DMA-buf deregistration race. Blocked by: STL-76982 (DMS unregister, Verify) STL-76983 (force-cancel trackers, Open) STL-76984 (rvt/bulksvc race, Open) | Retest with next DST once all 3 blockers land.
STL-76880 | P0 | mi300x GPU kernel panic rvt_send_complete | Simonson | In Progress | Same rdmavt DMA-buf path as 76950. | Likely fixed by 76950 patches. Retest together.
STL-76940 | P0 | LNetError RDMA timeout with BTS — Lustre client eviction | Simonson | In Progress | Lustre ko2iblnd hits BTS verbs path. Caused by STL-76941 (Verify). Blocked by STL-76999 (Verify). | Zhu: "Wait for 12.1.2 DST — fixed a few bugs."
Verify Queue (5 P0 BTS fixes awaiting validation)
Issue | Summary | What It Fixes
STL-76999 | Fix bulksvc_dbg_open unbounded spin-wait deadlock | Blocks 76940 (Lustre RDMA timeout)
STL-76942 | bufcount error — BTS buffer management | BTS Lustre data integrity
STL-76863 | BAD WRITE CHECKSUM — BTS MR registration error | BTS Lustre data integrity
STL-76847 | calculate_mr_page_offset Invalid | BTS Lustre data integrity
STL-76732 | hfi1_dms_impl_dlist_remove crash — DMS list corruption | BTS internal locking

## Slide 3
OPX — Detail
3 active + 1 in Verify — TID cache is chronic; new GPU AI hang needs triage
Active (3 bugs)
Issue | Pri | Summary | Assignee | Status | Customer | Root Cause | Next Steps
STL-76365 | P0 | HPL hang in hfi1_user_exp_rcv_setup | Cernohous | In Prog | — | OPX TID cache diverges from kernel. Links to 76561, 76972, 76685, 76554. | Fix spans OPX user-space + hfi1 kernel.
STL-73247 | P0 | sph_exa hang with OPX Open MPI | Erwin | In Prog | — | Same TID cache root cause. Open since 12.1.0.x. | Same fix as 76365.
STL-77071 | P0 | MPT-30B hang aws-ofi dmabuf | Espinoza | Open | RWTH | Possibly OPX+DMA-buf. May be user config. | Engaging RWTH directly.
Verify Queue (1 OPX fix)
Issue | Summary | What It Fixes
STL-76561 | HPL OPX_TID_CACHE assert with use_bulksvc:N | Related to TID cache cluster (76365, 73247)

## Slide 4
Fabric / MYR FW — Detail
3 active — Buffer/credit cluster: 2 bugs, zero fixes landed. VR fault close to landing.
Active (3 bugs)
Issue | Pri | Summary | Assignee | Status | Customer | Root Cause | Next Steps
STL-76338 | P0 | tportPktDropPending hang on ISL bounce | Wright | In Prog | TACC | MYR Tport state machine. Links to 76651, 76652, ISS-8041. | Reproduced internally. Wright analyzing.
STL-76494 | P0 | Hung nodes — RbufCtrlSbe ECC errors | Rothermel | In Prog | TACC | SRAM bit errors corrupt buffer mgmt. sw_fixed label. Links to 76836, 77090. | SW workaround exists. Watch SBE rate for HW degradation.
STL-77092 | P0 | DWC switch VR fault (liquid-cooled) | Nagarajan | In Review | Lenovo | Voltage regulator HW fault. Separate from buffer/credit. | Fix in review.

## Slide 5
Host Driver + Link / 8051 FW — Detail
3 active — 76836 (LLNL ipoib) may be fabric-caused; 76873 (link training) feeds the picture
Active (3 bugs)
Issue | Pri | Summary | Assignee | Status | Customer | Root Cause | Next Steps
STL-76836 | P0 | ipoib timeout at LLNL Lynx | Novak | Open | LLNL | IPoIB/SDMA path. Links to 76494 (RbufCtrlSbe) + 76873 (link training). May be fabric-caused. | Correlate with fabric cluster. If fabric-side, reclassify.
STL-76997 | P0 | Job crashes during SPEC run | Luick | Open | NEC/RWTH | Relates to 75193 (PCIe fatal error). Investigating uncorrectable error correlation. | Koch providing lspci. Luick proceeding with investigation.
STL-76873 | P0 | Link fails LNI EstablishComm.TxRxHunt | Johanson | In Prog | LLNL | 8051 FW SerDes link training. ~8 links not coming up. Links to 76836 (ipoib). | Johanson leading via Link Working Group.

## Slide 6
Root Cause Cluster Summary (P0 Only)
12 active P0 bugs → 8 root causes | 6 in Verify | 5 Closed
# | Root Cause | Active | Verify | Closed | Fix One, Fix All?
1 | BTS DMA-buf deregistration race | 3 | 5 | 1 | Yes — 76950 fix in review → cascade-fixes. But 2 of 3 blockers still Open.
2 | OPX TID cache kernel divergence | 2 | 1 | — | Yes — same arch fix. Complex (user + kernel).
3 | MYR buffer/credit switch FW | 2 | — | — | Partially — ISL drops + RbufCtrlSbe related but may need separate fixes. Zero resolved.
4 | MYR VR fault | 1 | — | — | Standalone — HW issue. Fix in review.
5 | OPX GPU AI (DMA-buf) | 1 | — | 1 | TBD — 77071 may be user config. 76946 closed Invalid.
6 | IPoIB timeout | 1 | — | — | Maybe fabric-caused — links to 76494 + 76873. If confirmed, reclassify.
7 | PCIe / host driver crash | 1 | — | — | Standalone — investigating uncorrectable error correlation.
8 | Link training 8051 FW | 1 | — | — | Standalone. Link WG owns.
— | Resolved standalone | — | — | 3 | 76733 (Done), 76745 (Done), 76727 (Not A Defect), 77078 (User Verified)
1. BTS is #1 area — 3 active + 5 in Verify. 76950 fix depends on 2 patches still Open (76983, 76984). Next DST is the gate.
2. MYR buffer/credit has zero fixes landed — 2 P0 bugs (76338, 76494), both In Progress. TACC is primary customer.
3. 76836 (LLNL ipoib) may be fabric-caused — links to 76494 (RbufCtrlSbe) + 76873 (link training). If confirmed, reclassify.
4. OPX TID hangs still chronic — 73247 open since 12.1.0.x. Architecturally complex fix.
5. 77071 (RWTH GPU AI hang) is new this week — may be user config, needs triage before committing resources.